## Slide 1
Internet of Things for Sensing the School’s Environment
Sensors 101

## Slide 2
Contents
Introduction
Sensors 101
Fundamentals
Sensor Circuit
Practice
Project Sensors
Dust Sensor
BME680
MQ5 (Gas)
Light Sensor

## Slide 3
Fundamentals
Can you think of any sensors?
Acoustic, sound, vibration
Automotive Sensors
Chemical Sensors
Electric current, electric potential, magnetic, radio
Environment, weather, moisture, humidity
Flow, fluid velocity
Ionizing radiation, subatomic particles,
Navigation instruments
Position, angle, displacement
Optical, light, imaging, photon…….
There are so many more sensors that have not been listed.
For more go to https://en.wikipedia.org/wiki/List_of_sensors
Notes: So can you think of any sensors? Hints: Thermometer, Gigacounter, pressure sensor, Ph sensor, Light sensor Volt/Amp meter
There are so many types and variations from analogue to digital (glass thermometer, electronic thermometer).

## Slide 4
Expanding on the previous slide, a sensor is a essentially a voltage divider circuit, which is used to measure difference between Vin and Vout a typical circuit shown below.
So by using the known input voltage and the and resistor values the output voltage can be calculated using this formula.
We are measuring the change in resistance (R1) from an unknown phenomenon.
or
Sensor Circuit
Notes: A sensor circuit is essentially a voltage divider with either resistors, capacitors or inductive components.
This a resistive voltage divider and is sensing that which is present. Say sunlight, as light increases so does the resistance. The higher the Vout the more light there is. The name for this component is called a Light dependant resistor (LDR)
Voltage in (Vin) is the source say 5v and the Voltage out (Vout).
R1 is the LDR and R2 is a normal resistor.
This formula is used in some of our sensors.

## Slide 5
Practice
Solve for in each circuit, the formula is:
1.64v
=
v
v
5v
2.64v
3.3v
=
=
19.1v
=
Notes: Voltage is V
Resistance is Ohms represented as
Half a mark if the symbols are missing.
2.64v
15.22v
0.00v
4.94v or 5.00v depending on the calculator (the equation should be re arranged or transposed to make Vin the subject: appears with answer.
Voltage is V
Resistance is Ohms represented as Ω
Half a mark if the symbols are missing.
2.64v
15.22v
0.00v
4.94v or 5.00v depending on the calculator (the equation should be re arranged or transposed to make Vin the subject: appears with answer.

## Slide 6
The Microcontroller a is device that can process one action at a time. For this project we are using the providing power for a Ardunio MKR1010 WiFi. Other than sending our data over WiFi and sensors it serves another function.
Analogue to Digital Converter
That function is the Analogue Digital Converter (ADC) this takes the voltage reading as wave, much like the right hand side of the icon and converts into a number consisting of 1s and 0s (Binary)
Notes: A sensor circuit is essentially a voltage divider with either resistors, capacitors or inductive components.
This a resistive voltage divider and is sensing that which is present. Say sunlight, as light increases so does the resistance. The higher the Vout the more light there is. The name for this component is called a Light dependant resistor (LDR)
Voltage in (Vin) is the source say 5v and the Voltage out (Vout).
R1 is the LDR and R2 is a normal resistor.
This formula is used in some of our sensors.

## Slide 7
Project Sensors
Dust Concentration Sensor
Light Intensity Sensor
MQ5 Gas Sensor
BME680 Pressure, Humidity and Temperature, VOC Sensor
Notes: Here are the sensors we are going to use, and we will talk about how each one functions.

## Slide 8
Dust Sensor
Good indication of the air quality in a environment by measuring the dust concentration.
Unit: pcs/L or pcs/0.01cf.
The Particulate Matter level (PM level) in the air is measured by counting the Low Pulse Occupancy time (LPO time) in given time unit.
LPO time is proportional to PM concentration. This sensor can provide reliable data for air purifier systems; it is responsive to PM of diameter 1μm.
This sensor uses counting method to measure dust concentration, not weighing method
Get Con
Get Con
520 pcs/0.01cf
Example
Notes: The dust sensor is fairly complex but for basically it uses a laser to measure the dust particles falling through the laser beam.
Dust, pollen, pollution (soot) etc is called Particulate matter.
Low occupancy is the amount of time there is dust blocking the laser beam in an amount of time.
Notice con in red is the Concentration. Duration and LowOcc is in ms milli-seconds
Unit is Particles (pcs) per 0.01 cubic feet

## Slide 9
MQ5 Gas Sensor
The Grove - Gas Sensor(MQ5) module is useful for gas leakage detection (in home and industry).
It is suitable for detecting Hydrogen (H2), Liquid Petroleum Gas (LPG), Methane (CH4), Carbon-dioxide (C0) and ethanol/methanol.
Graph shows how different readings means different gases have been detected. Note RS/R0 is the ratio between that which has been sensed and the normalised ideal condition.
Get actual ratio
Get Ro
There is no one simple linear equation for the graph however, the Ro is worked out during a testing phase and then used in the actual implementation to get the ratio or RS/RO
Notes: This sensor composed of a micro AL2O3 ceramic tube, Tin Dioxide (SnO2) sensitive layer, measuring electrode and heater which are fixed into a
crust made by plastic and a stainless steel net.
Used to measure a range of gases.
Math involved consists of several dividing functions. First R0 and Rs_air are found using a ADC formula. Then the ratio is found, this ratio is between 0.1 and 10, see graph.
There is no linear formula for this, however manual interpretation of the graph we can get the values of each gas parts per million. There is a way to do this in code, but that is for later.

## Slide 10
Light Level Sensor
The Grove - Light sensor integrates a photo-resistor(light dependent resistor) to detect the intensity of light. The resistance of photo-resistor decreases when the intensity of light increases. The output signal is analogue value, the brighter the light is, the larger the value.
This module can be used to build a light controlled switch i.e. switch off lights during day time and switch on lights during night time.
If a door has been opened during the day
Sun light in a greenhouse
A robot that reacts to light
Notes: This is the simplest sensor, a photodiode is put next to a resistor just like a voltage divider circuit.
We take the value and then assign some meaning to it such as 900 ADC is bright, 200 or lower is dark.

## Slide 11
BME680 Sensor
Grove – The BME280 is high-precision, low-power combined humidity, pressure, and temperature sensor. As the atmospheric pressure changes with altitude, it can also measure approximate altitude of a place.
Temperature sensor measurement range: -40 ℃ to 85 ℃, with ±1.0°C accuracy
(You can do the conversion for Fahrenheit or Kelvin)
Celsius to ℃
Ceclius to Fahrenheit,
Humidity sensor measurements range: 0% - 100% relative humidity , with ±3% accuracy
Atmospheric pressure sensor measurement range: 300 - 1100 hPa with ±1.0 hPa accuracy