## Slide 1
Internet of Things for Sensing the School’s Environment
Sensors 101

## Slide 2
Contents
Introduction
Sensors 101
Fundamentals
Sensor Circuit
Practice
Project Sensors
Dust Sensor
BMP280
MQ5 (Gas)
Light Sensor

## Slide 3
Fundamentals
Can you think of any sensors?
Acoustic, sound, vibration
Automotive Sensors
Chemical Sensors
Electric current, electric potential, magnetic, radio
Environment, weather, moisture, humidity
Flow, fluid velocity
Ionizing radiation, subatomic particles,
Navigation instruments
Position, angle, displacement
Optical, light, imaging, photon…….
There are so many more sensors that have not been listed.
For more go to https://en.wikipedia.org/wiki/List_of_sensors
Notes: This project aims to provide you with a thorough introduction to IoT.
It introduces the key concepts of IoT, necessary in using and deploying IoT systems.
Furthermore, the application of physical computing to sense the environment around you

## Slide 4
Expanding on the previous slide, a sensor is a essentially a voltage divider circuit, which is used to measure difference between Vin and Vout a typical circuit shown below.
So by using the known input voltage and the and resistor values the output voltage can be calculated using this formula.
We are measuring the change in resistance (R1) from an unknown phenomenon.
or
Sensor Circuit

## Slide 5
Practice
Solve for the unknown variable in each circuit, the formula is for you reference.
5V
1.64V
=
3.1V
=
5V
5V
=
2.64V
3.3V
=

## Slide 6
Project Sensors
Dust Concentration Sensor
Light Intensity Sensor
MQ5 Gas Sensor
BME280 Pressure, Humidity and Temperature Sensor

## Slide 7
Dust Sensor
Good indication of the air quality in a environment by measuring the dust concentration.
Unit: pcs/L or pcs/0.01cf.
We can see the concentration of dust is very low in the evening, but it is higher in the afternoon
The Particulate Matter level (PM level) in the air is measured by counting the Low Pulse Occupancy time (LPO time) in given time unit.
LPO time is proportional to PM concentration. This sensor can provide reliable data for air purifier systems; it is responsive to PM of diameter 1μm.
This sensor uses counting method to measure dust concentration, not weighing method

## Slide 8
MQ5 Gas Sensor
The Grove - Gas Sensor(MQ5) module is useful for gas leakage detection (in home and industry).
It is suitable for detecting H2, LPG, CH4, CO, Hydrogen (H2), Liquid Petroleum Gas (LPG), Methane (CH4), Carbon-dioxide (C0) and ethanol/methanol.
The sensitivity of the sensor can be adjusted by using the potentiometer.
This sensor should only be used for approximation

## Slide 9
Light Level Sensor
The Grove - Light sensor integrates a photo-resistor(light dependent resistor) to detect the intensity of light. The resistance of photo-resistor decreases when the intensity of light increases. The output signal is analog value, the brighter the light is, the larger the value.
This module can be used to build a light controlled switch i.e. switch off lights during day time and switch on lights during night time.
If a door has been opened during the day
Sun light in a greenhouse
A robot that reacts to light

## Slide 10
BME280 Sensor
Grove – The BME280 is high-precision, low-power combined humidity, pressure, and temperature sensor. As the atmospheric pressure changes with altitude, it can also measure approximate altitude of a place.
Temperature sensor measurement range: -40 - 85 ℃, with ±1.0°C accuracy
(You can do the maths for Fahrenheit or Kelvin)
Humidity sensor measurements range: 0% - 100% relative humidity , with ±3% accuracy
Atmospheric pressure sensor measurement range: 300 - 1100 hPa with ±1.0 hPa accuracy