## Slide 1
Internet of Things for Sensing the School’s Environment
Sensors 101

## Slide 2
Contents
Introduction
Sensors 101
Fundamentals
Sensor Circuit
Practice
Project Sensors
Dust Sensor
BMP280
MQ5 (Gas)
Light Sensor

## Slide 3
Fundamentals
Can you think of any sensors?
Acoustic, sound, vibration
Automotive Sensors
Chemical Sensors
Electric current, electric potential, magnetic, radio
Environment, weather, moisture, humidity
Flow, fluid velocity
Ionizing radiation, subatomic particles,
Navigation instruments
Position, angle, displacement
Optical, light, imaging, photon…….
There are so many more sensors that have not been listed.
For more go to https://en.wikipedia.org/wiki/List_of_sensors
Notes: This project aims to provide you with a thorough introduction to IoT.
It introduces the key concepts of IoT, necessary in using and deploying IoT systems.
Furthermore, the application of physical computing to sense the environment around you

## Slide 4
Expanding on the previous slide, a sensor is a essentially a voltage divider circuit, which is used to measure difference between Vin and Vout a typical circuit shown below.
So by using the known input voltage and the and resistor values the output voltage can be calculated using this formula.
We are measuring the change in resistance (R1) from an unknown phenomenon.
or
Sensor Circuit

## Slide 5
Practice
Solve for the unknown variable in each circuit, the formula is for you reference.
5V
1.64V
=
3.1V
=
5V
5V
=
2.64V
3.3V
=

## Slide 6
Project Sensors
Dust Concentration Sensor
Light Intensity Sensor
MQ5 Gas Sensor
BME280 Pressure, Humidity and Temperature Sensor

## Slide 7
Dust Sensor
Good indication of the air quality in an environment by measuring the dust concentration.
The Particulate Matter level (PM level) in the air is measured by counting the Low Pulse Occupancy time (LPO time) in given time unit.
LPO time is proportional to PM concentration. This sensor can provide reliable data for air purifier systems; it is responsive to PM of diameter 1μm.
This sensor uses counting method to measure dust concentration, not weighing method
Unit: pcs/L or pcs/0.01cf.
We can see the concentration of dust is very low in the evening, but it is higher in the afternoon

## Slide 8
MQ5 Gas Sensor
The Grove - Gas Sensor(MQ5) module is useful for gas leakage detection (in home and industry).
It is suitable for detecting H2, LPG, CH4, CO,
  Hydrogen (H2), Liquid Petroleum Gas (LPG), Methane (CH4), Carbon-dioxide (C0) and ethanol/methanol.
The sensitivity of the sensor can be adjusted by using the potentiometer.
Approximation
Unit: pcs/L or pcs/0.01cf.

## Slide 9
Internet of Things for Sensing the School Environment Project